## Slide 1: Pacific school of engineering
(civil department)
Linear measurement
Guided By:-
Hiten Kheni
Jasmin Gadhiya
Group name:- J

## Slide 2: Topic to be covered
Chaining
Instrument used in chaining
Ranging
Offsets
Error in chaining

## Slide 3: Chaining
In the method of chaining to denote horizontal distance, either a chain or a tape is used for making direct measurements.
A chain is less precise then a tape and therefore works with precision a tape is used.

## Slide 4: Instrument used in chaining
Chain and tape
Pegs
Arrows
Ranging rod
Plumb bob

## Slide 5: Chain
The chain is made of straight links of galvanized mild steel wire of 4mm in diameter.
The links are bent into rings at the ends because of which they offer flexibility.
The end of the chain are provided with brass handle at both ends.
The length of the chain includes both the handles.
Brass tallies is are provided at every 5 meter of the chain.

## Slide 6: tapes
tapes
Cloth or linen tape
Steel tape
Invar tape
Metallic tape

## Slide 7: Types of taps
Cloth or linen tape
The linen tape can be used for taking subsidiary measurement of offsets.
This tapes available in 10m,20m and 30m length.
This tapes are made varnish strip of woven linen 12mm to 15mm wide.
This tapes are calibrated in ‘m’ and ‘cm’.

## Slide 8: Metallic tape
This tape is made varnished strip of fine brass, copper or bronze wires.
It is better than linen tape.
This tapes are available in 5m,10m,15m and 50m length.
This tapes are calibrated in ‘m’ and ‘cm’.

## Slide 9: steel tape
Steel tape is superior to a cloth or metallic tape and consist of a light strip of width 6mm to 10mm.
Steel tape are available in 2,5,10,30 and 50m length.

## Slide 10: Invar tape
Invar tape are used for linear measurement of a very high degree and of precision.
The invar tape is made of alloy of nickel and steel.

## Slide 11: pegs
Pegs are made of timber or steel and they are used to mark the position of the station or terminal points of survey line.
Pegs are 15cm long and are driven in ground with the help of hammers.

## Slide 12: Arrows
Arrows are made of good quality hardened and tempered steel wire of 4mm in diameter.
The length of arrow is 40cm.
One and of the arrow is made sharp and the other end is bent in to a loop of facilitate carrying of arrows.

## Slide 13: Ranging rod
The ranging rod are generally 2 to 3m in length.
These rods are paints with white and black or red and white colour in 20cm.
plumb bob
A plumb bob is used to transfer the points to the ground.

## Slide 14: ranging
Direct ranging
Indirect ranging
By eye
By line ranger

## Slide 15: Indirect ranging
This method ranging is adopted when the two ends of survey line are not visible from either of the station due to a hill or high ground between them.
Point a1 is not visible point a2 and a2 is not visible point a1. the proceed in straight line between a1 and a2,the process of indirect ranging is done.
a1
a2
m1
m2

## Slide 16: Offset
Perpendicular offset
Swing offset
Long offset
Short offset
Oblique offset

## Slide 17: Perpendicular offset
When distance are measured at right angle(90) then such distance are called as perpendicular offsets or only offset.
q
p
a
b
90
q
a
b
p

## Slide 18: Oblique offset
When distance are measured other than 90, then such distances are called as oblique offset.
Short offset
When offset are set out by swinging the tape on chain line,it should not be longer then 15m,such offset are known as short offset.
Offset should be as short as possible, however limiting length of offset depends upon accuracy desired, nature of ground, scale of plotting.

## Slide 19: Long offset
Offset which are more than 15m are set by optical square or cross staff, such offsets are known as long offsets.
Swing offset
Offset taken by swinging tape or chain is called swing offset.

## Slide 20
Thank you